INSTALLATION MANUAL

EUROCOM M2 Communication System

for fitment on BMW K1200LT

KIT K-LTM2

TO OBTAIN OPTIMUM PERFORMANCE FROM YOUR SYSTEM,

READ AND UNDERSTAND THESE INSTRUCTIONS PRIOR TO USE.

UNDERSTANDING YOUR SYSTEM

KIT CONTENTS:

1 Eurocom M2 intercom unit

1 Bike stereo interface lead

1 installation accessory kit

2	Standard headsets

(style varies with kit)

2	Coiled headset extension leads

2	Wind sock kits

2	Foam speaker spacers (Pairs)

EUROCOM M2 INTERCOM

The unit has four leads:

RIDER LEAD: Black-lead with black socket 1300mm (50’) long.

PASSENGER LEAD Black-lead with black socket 400mm (15-3/4") long.

AUXILIARY LEAD: Black-lead with grey socket 400mm (15-3/4”) long.

POWER LEAD: Twin Red/Black lead 1000mm (39”) for connection to a 12 volts.

There are two input sockets and a knob on the unit faceplate:

REMOTE SWITCH SOCKET for connecting optional high/low

handlebar switch.

MUSIC SOCKET for connecting an audio source.

VOX SETTING KNOB for adjusting the VOX baseline setting.

STANDARD HEADSET

The headset has a microphone on a flexible boom (available in different length booms for specific helmet fitment) and two speakers to provide stereo music reproduction when the system is connected to a suitable music source. The speakers are covered with replaceable hygienic foam covers. The headset is designed to be a semi-permanent installation in a motorcycle helmet. Using the headset for purposes other than those described is not covered by warranty.

HEADSET EXTENSION LEAD

Connects the lead from the headset to the appropriate lead from the intercom unit.

BIKE STEREO INTERFACE LEAD

Connects the on-board stereo system to the Eurocom M2.

WIND SOCK KIT

For use with an open face helmet or a helmet that vents directly on the microphone.

FOAM SPEAKER SPACERS (1/4”)

Positions speakers closer to the ears in helmets with large ear cups (notably open face helmets)

INSTALLATION ACCESSORY KIT

Includes a variety of items that may be required in order to properly install the Eurocom M2 on the bike for 12 volt operation.