PREPARING THE SYSTEM

FITTING THE EUROCOM M2 INTERCOM UNIT

Examine how the seat fits on the bike so as not to trap, pinch, or rub any of the leads when reinstalling the seat sections. Lift driver’s seat and remove the two (2) 5mm alIen head screws securing the passenger seat and remove the passenger seat. Velcro the Eurocom M2 with the included Cosmalon® to the flat area just outside the frame rail under the left side of the passenger seat.

CONNECTING THE POWER LEAD

Attach the black (negative) wire directly to the ground terminal on the battery with the supplied eyelet. Attach the red (positive) wire to the tail light fuse located under the passenger seat. (Any other fuse which turns on/off with the key may be used.) The positive (RED) 12-volt power lead should be connected to a fused, switched power circuit. Alternative connection points include the rear taillight feed. Please check with a qualified electrician and/or your bike supplier for additional information.

ROUTING RIDER AND PASSENGER LEADS

Route and secure the driver’s lead between the gas tank and driver’s. Route and secure the passenger lead between the passenger’s seat and driver’s seat. Position the leads to ensure that they do not fall onto or near any hot surfaces or moving parts. Avoid routing the leads near sources of possible interference (ignition coils, HT leads, fuel injection pumps etc...). Ensure that excess pressure is not applied to the lead particularly when on the bike.

AUXILIARY LEAD

If you are connecting a two-way device to the auxiliary lead decide where you will carry the device and route the auxiliary lead appropriately. If you are not connecting any auxiliary equipment via the auxiliary lead secure the lead in a safe location. An optional auxiliary extension lead (EL-T-B) is available to extend the socket to remote location.

CONNECTING THE BIKE STEREO

Attach the Bike Stereo Interface Lead (SML-CR-A) as follows:

a.	Locate the 12 wire round connector under the passenger seat.

b.	Solder one (1) white wire* to the yellow wire from the connector.

c.	Solder one (1) red wire to the yellow wire with blue trace from the connector.

d.	Solder the other white wires* to the blue wire with grey trace from the connector.

e.	Solder the remaining red wires to the blue wire with purple from the connector.

f.	Insert the 3.5mm plug into the music jack on the Eurocom M2.

(*: Some Bike Stereo Music Interface units contain blue wires in place of white.)

FITTING THE HEADSETS

Before fitting the headsets into your helmets connect them to the intercom and test the system for proper installation. Refer to the included headset instructions to fit the headsets. Pay particular attention to correct positioning of the microphone and speakers.

1 you have any questions concerning the installation process contact your supplying dealer.

USING YOUR SYSTEM

With the headsets installed connect the extension leads to the helmets and to the sockets of the Eurocom M2 now installed on the bike. Switch on the bike and the system will be ready to use. It is not unusual for first-time users to experience difficulty activating the system. The Eurocom M2 utilizes advanced VOX (Voice activation) circuitry that is designed to cut unwanted noises. Inaccurate use of the headset will result in an appropriate response from the system. . . cutting the noise.. which it may judge to be the user’s voices. See the headset manual for detailed information on headset installation and use. The system will, also, automatically mute the music and/or send a transmit signal to a suitably equipped two-way radio transceiver, if connected.

ADJUSTING THE VOX SETTING

it you are experiencing difficulty activating the system first adjust microphone/speaker positioning, talk more positively and practice headset use. VOX adjustment should only be made to set the