Weather Information Sheet

| WEATHER REPORT | ISSUED | AGE WHEN RECEIVED | VALID PERIOD |
| --- | --- | --- | --- |
| Aviation Routine Weather Report (METAR) | HOURLY (50 to 55 past Hr.) | Few minutes up to 30 minutes | Until next METAR or SPECI is issued |
| RADAR Weather Reports (SD) | HOURLY (35 min past Hr.) | Approximately 20 minutes | Until next SD is issued |
| Pilot Weather Report (PIREP) | AS OBSERVED | Few minutes | Observed Data |
| Terminal Aerodrome Forecast (TAF) | 0000z, 0600z, 1200z, 1800z | Forecasted Data | 24 Hr. forecast |
| Winds and Temperature Aloft Forecast (FD), (CHART) | 0000z, 1200z | Forecasted Data | Time interval of use is stated on the forecast |
| Area Forecast (FA) | 0045z, 0845z, 1745z | Forecasted Data | Total 18 Hrs., Synopsis 18 Hrs 12 Hr. forecast with 6 Hr. Outlook |
| AIRMETS (WA) | Every 6 Hrs. | Observed with forecasted data | Maximum forecast period is 6 Hrs. |
| SIGMETS (WS) | When specific SIGMET weather phenomena occur | Observed with forecasted data | Maximum forecast period is 4 Hrs. |
| Convective SIGMETS (WST) | HOURLY (55 past Hr.) | Few Minutes | Until next WST or 2 Hr. Outlook 2 to 6 Hrs. |
| Surface Weather Analysis (CHART) | Every 3 Hrs. | 1.5 to 2 Hrs. | Observed Data |
| RADAR Summary (CHART) | HOURLY (35 past Hr) Accumulated from SDs | 1 Hr. | Until next SD reports |
| Weather Depiction (CHART) | Every 3 Hrs. | Approximately 60 to 80 minutes | Observed Data |
| Low Level Significant Weather Prognostic (CHART) | 0000z, 0600z, 1200z, 1800z | Forecasted Data | Left Panels – 12 Hrs. Right Panels – 24 Hrs. |
| Composite Moister Stability (CHART) | 0000z, 1200z | Approximately 1 Hr. | Observed Data |
| Serve Weather Outlook (CHART) | 0800z | Forecasted Data | Left Panel – 1st 24Hr Period Right Panel – 2nd 24Hr Period |
| Constant Pressure Analysis (CHART) | 0000z, 1200z | 2 to 3 Hrs. | Observed Data |