Tombstone

Tombstone is a Dory-ish one sheet boat. The rear transom is made out of scrap or 1x lumber. Waterline is at 200 lbs displacement, with a boat weight of  35 lbs or so. Good for a kid or light adult. Stitch and Glue construction. Seating up to the builder. Not recommended for sail.

| Bottom Panel Half |
| --- |
| Station | X | Y | X2 | Y2 |
| 1 | 0 | 0 | 0 | 3 15/16 |
| 2 | 12 | 0 | 12 | 8 1/2 |
| 3 | 24 | 0 | 24 | 11 1/16 |
| 4 | 36 | 0 | 36 | 12 |
| 5 | 48 | 0 | 48 | 11 7/8 |
| 6 | 60 | 0 | 60 | 10 3/4 |
| 7 | 72 | 0 | 72 | 7 11/16 |
| 8 | 84 | 0 | 84 | 2 3/8 |
| 9 | 87 7/8 | 0 | 87 7/8 | 0 |
| Side Panel First Chine |
| Station | X | Y | X2 | Y2 |
| 1 | 0 | 2 3/16 | 0 | 9 5/16 |
| 2 | 12 | 15/16 | 12 | 10 3/16 |
| 3 | 24 | 5/16 | 24 | 10 11/16 |
| 4 | 36 | 0 | 36 | 11 1/16 |
| 5 | 48 | 0 | 48 | 11 5/16 |
| 6 | 60 | 5/16 | 60 | 11 3/8 |
| 7 | 72 | 3/4 | 72 | 11 1/4 |
| 8 | 84 | 1 9/16 | 84 | 10 7/8 |
| 9 | 91 1/8 | 2 3/16 | N/A | N/A |
| 10 | N/A | N/A | 95 | 10 3/8 |
| Transom Half |  |  |
| Station | X | Y |  |  |
| 1 | 0 | 3 15/16 |  |  |
| 2 | 6 7/8 | 5 13/16 |  |  |

All measurements are in inches. The end points of the plotted lines are joined by a straight line.

This shows how the measurements are used to lay out the panels. X and Y are the bottom line of the panel and X2 and Y2 are the top line. All points are from the edge of the ply or a baseline. Any points which are N/A are not plotted. They may just be not on the panel or are not important to that line. The two end points are closed with a straight line.

For information on Stitch and Glue, please check the construction of fisher10. The hull was done entirely with stitch and glue, except for the transom/side panel joint, which was first attached with screws and then filleted on the inside and taped on the outside. There are also many good sites with Stitch and glue information. www.bateau.com has an excellent primer on the subject, so do most of the other major plans dealers, such as Glenn-L and Clark Craft.