;
; warning : at this point I have seen some undefined behavior with the
;    debugger when running under windows 95.  Basically, one of the
;    registers gets set to an arbitrary value at the end of
;    each go or trace.  Which register is affected seems somewhat
;    random, although it is predictable for a particular program.
;
;    for now, I recommend if you need to debug with the debugger, exit 
;    windows rather than running in a DOS shell.  It is much better 
;    than it was but still happens occasionally.  Rebooting windows
;    seems to help
;


1) debugger
	Later I will add an external debugger to the system, but, for now you
	can build a debug-like debugger into your programs when linking
	with TLINK by using the startup file C0DOSD instead of the startup
	file C0DOS.  When you build with this alternate startup file it
	will pull the debug kernel in from the CLDOS library.  At this point,
	running the program will bring you to a DEBUG prompt, and the
	EIP register will be set to the first instruction of your
	main() subroutine.  The command line will have been parsed at
	this point and the C RTL will have been initialized.

	Note: I have NOT been able to get this debugger to work with
	the watcom linker.  But, Kirill Joss has set up the watcom startup
	files so that WDEBUG should work with images linked with the
	watcom linker.

2) command line interface

	the command line interface is similar to that of debug.  However,
	some enhancements have been made:

	a) knows the names of ALL registers and allows you to use them
	   anywhere a number is allowed.  It knows 8, 16, and 32-bit
	   register names... (this is a non-segmented debugger)

	b) it knows how to parse string values and convert them to hex.
	   so, a quoted string can be used anywhere a non-address value
	   can be used.  HOWEVER, in most cases strings longer than
	   4 characters will be truncated.  Also, some commands
	   (notably fill) will only use the least significant value
	   of the number and will truncate it to one character

	c) commas are always treated like spaces.


3) Commands

Here is a brief list of commands:

a                              - assemble
b  [#]                         - Show breakpoint(s)
b  [-]#,addr                   - set or clear a breakpoint
c  source,dest,len             - compare memory
d  [start [,end]]              - dump memory
e  start [,list]               - examine memory
f  start,end [,val]            - fill memory
g  [=start] [,break]           - run from start (or pos) to break
h  val1 [+-*/] val2            - hex arithmetic
i  port                        - read from port
m  source,dest,len             - move memory
n  [s]                         - show fp regs/status
o  port,val                    - write to port
p  [r][n]                      - step through
q                              - quit
r  [reg[:val]]                 - show/modify regs
s  start,end [,list]           - search for a byte pattern
t  [n] [count]                 - step into
u  [start [,end]]              - unassemble
?                              - this help

Many of the commands are similar to what DEBUG does.  Note that
the ',' character is always optional.  Following is a detailed description 
of each command:

a <CR>
	assemble code

b <CR>  
	show active breakpoints.  
	this Does nothing if no breakpoints are active.

b# <CR>  
	where '#" is any number from 0-0F.  
	this Shows the value of that breakpint.

b # , address <CR> 
	where '#' is a hex number from 0 to 0F and
	address is any valid address.  Sets a breakpoint.  At run time
	an 'int 3' will be inserted at the address.  Note that breakpoint
	0 is a special breakpoint used by the 'go' command; it will be
	automatically cleared at the end of the next go/trace/proceed.

b-# <CR>
	clears a breakpoint
		     
note on breakpoint commands:
	the debugger DOES do hardware breakpoints, and will show you
	the approximate syntax on the help screen.  However, this
	capacity can only be used if windows has been shut down due
	to my inability to get at the paging tables.

c source, dest, len <CR>
	compare blocks source and dest for len len

d <CR>	
	disply 80h bytes starting at the current location

d addr <CR> 
	display 80H bytes starting at addr

d addr,addr <CR>  
	display all the bytes between the two addresses.  The
	second address may NOT be qualified with a segment.

e addr	<CR> 
	start prompting for data.  Note: you CAN quote a character
	here.

e addr , list of data <CR>
	put the indicated data at the address.

f addr , addr <CR>
	fills all the bytes between the two addresses with 0.
	the second address may NOT be qualified with a segment

f addr , addr , value <CR>
	fills all the bytes between the two addresses with value

g = addr <CR>
	start executing at address

g addr <CR>
	start executing at current IP, set a temporary breakpoint
	at addr (overwrites breakpoint 0)

g =addr , addr <CR>
	start executing at the first address, set a breakpoint at the
	second address

h val [op] val <CR>
	do some math.  Valid operators are : +-*/%.  If no operator
	is given, + will be assumed

i port <CR>
	show the value at the port

m source, dest, len <CR>
	move memory from source to dest with length len

n <CR>
	show fp registers.  The TOS register will have a star next to
	it.  Note: if you have a 386 with no coprocessor you will get an
	error message.

ns <CR>
	show fp status.  Shows masked exceptions, active exceptions,
	rounding/precision selections, and status of the C? flags.  Note:
	if you have a 386 with no coprocessor you will get an error message.

o port, val <CR>
	output a value to a port

p <CR>
	step over subroutines, string instructions, int calls.  For
	loop instructions, it runs until the loop falls through.  This is
	a DESTRUCTIVE instruction, it modifies the code stream temporarily
	if a simple trace won't do.

pr <CR}
	proceed until the end of this subroutine.  traces until it
	hits a ret or iret, netsing is maintained.  Calls and interrupts
	and repeat string instructions run at full speed.  Note that
	when it stops you will be after the subroutine call instruction.

	warning: I am not sure what happens with recursion.  Also in
	(vanishingly) rare instances involving run-time stack switches
	this will halt with a garbled CS:IP.

q <CR>
	exit debugger

r <CR>
	show registers

r reg <CR>
	prompt for a new value for reg

r reg , value <CR>
	stuff a new value in reg

s addr , addr , list <CR>
	search.  List may be any combination of quoted strings and hex
	values.  Note: you MAY use a segment value in the second
	argument.  The segment of the result will be adjusted any time
	the offset of the first argument is greater than 8000h.

t <CR>
	step into instruction

t count <CR>
	single step for count instructions

u  <CR>
	disassemble from current location.  Location gets set to CS:IP
	each time an R command or trace/go is executed.

u addr <CR>
	dissassemble from address

u addr, addr <CR>
	disassemble code between the two addresses.

? <CR> help

4) running the debugger

	the debugger may ONLY be used with the default setup, that is
with tran's pmode 307/308.  If you use wlink and another dos extender,
you will have to use the watcom debugger.

	at this time the debugger is distributed as part of the run-time
	libraries and actually gets built into your code when you
	want to debug.  The mechanism is to replace the link file
	c0dos.obj with the file c0dosd.obj in the linker command line.
	This will ink the debugger in and activate it when you run
	your program.

	the debugger is a 32-bit debugger very similar to debug.  No
	symbolic debugging information is presently available; there are
	some tips for coping with this situation in the next section.
	Bear in mind this is a flat-mode debugger, but on occassion the
	run-time libraries actually switch segments around.  Be
	careful if you single-step through such code!

	When the program comes up, the EIP will be positioned to
	the beginning of the MAIN routine of your program.  At this time
	the c0dos module will have been run, resulting in the following:

	BSS initialized to zero
	#pragma startup functions executed
		in particular command line and environment params will
		be ready and stacked.  Also signal handling and such
		will be redirected to the debugger in case of an error.
	initial heap allocated from OS

5) debugging tips

	debugging without symbolic information is not the same
	as debugging with symbolic information.  The hardest part is
	if you are stepping through the program you have to rely on
	memory to know where you are.

	There are two basic strategies depending on your situation.
	The first is to place an int 3 instruction in your source
	code to stop the debugger at a certain place so you can
	examine memory and the registers.  While you can place
	the int3 instruction straight into the C source code, you
	may have to read the assembly source code for that module
	to get familiarized with what the compiler is doing at that
	point.  If you do enough of it you will grow accustomed to
	the kind of code the compiler generates and not have to consult
	the asm files so much.

	To put an int3 instruction in your C source code takes the following
	syntax:

	asm int3   /* this is best works for NASM */
	asm int 3  /* this works for TASM */

	the other strategy is primarily useful if you already know
	where the program is faulting; for example you get a general 
	protection fault.

	In such a situation, get the linker to generate a detailed
	map file (-map option of valx or the -m+ option if using CL386).
	then examine the map file looking for numbers near where
	it faulted and that will tell you what routine it faulted in.
	Note: if you have static functions they will NOT show up in
	the linker map file so there is some ambiguity here.

	I have used these techniques extensively to debug the tools
	in this package.  It is not as convenient as having symbolic
	information, but it sure beats printf statements and guessing!

6) notes on debugger

	the debugger was ported from my real mode debugger grdb.  GRDB
	is fairly stable and works very well; however I am NOT sure the port
	is 100% accurate.  the B and D and U and R and T and G and P 
	commands all work pretty well but I don't use other commands 
	as often.

	In particular I have only gone to certain lengths to test the
	built-in assembler, it basically works but I will not
	guarantee that it will work for all combinations of opcodes
	and operands.