THE SWAN NEWS

                                             October 1997 - Issue #8

FROM THE MANAGER:

Hello from snowy Utah.  Yes, we have about 3-4 inches of snow at this QTH, so what could be a better day for writing a newsletter?

I know it's been many moons since many of you have seen a "Swan News," and I hope you enjoy this one.  There will be some new items presented here, and by
popular request, I will also throw in some of the more helpful hints from the
past.

That way, if you have not received some of the earlier issues, you will be
provided with some of the more useful information.  Also be aware that there
is a web page on the Internet where the first 4 issues are available (in
condensed form) with more to come as Gary (VE4YH) finds time.  The Internet address is: http://www.pcs.mb.ca/~standard/

Having this wonderful tool is certainly helpful inasmuch as it provides an
opportunity for people World-Wide to receive the newsletter and other valuable information about Swan radios, including photos, historic data, etc.  It also provides yet another place to find other Swan enthusiasts and exchange e-mail.  Hope you all have a chance to visit the site Gary has provided.

In spite of some horrendous conditions, both nets seem to be doing well.  If
you frequent the Sunday net, you'll notice I have not been there much this
summer.  We continue to have a busy and rewarding life, and spent much of the
summer traveling.

First to the Midwest where we visited with family and took in two Indy car
(CART) races, and then for three weeks in Europe where we had a wonderful
visit and were pleased to find out that a memorial for the crew of my father's
B-24 bomber will be erected.  Six of his comrades were killed near where the
site of the moument will be located.  Dedication is scheduled for August 26th,
1998, the 54th anniversary, so I guess I'll be back for that.  Sorry to ramble
on about that subject, but I know several of you have been discussing this
W.W.II stuff with me over the years, and I wanted to let you know.

Our friend, Stu (K4BOV) has permanently planted his roots at his Corning, NY
QTH, so head your beams in that direction, and look for him on that great
Wednesday night technical net.

The net information is included later in this publication.  Hopefully you are
all well and enjoy the current issue.

******************************************************************************

KNOW THY SWAN  Part I by Stu Morrison/K4BOV

Many Swan single sideband transceivers became 36 years old this year.
Remarkably, this 1st generation of Swan radios and the 3 and 5 band units that
followed continue to maintain a significant presence in both American and
foreign amateur communities.  Few electronic devices for any purpose have achieved such tenure.

With the pool of capable tube era service technicians dwindling to near
nonexistence, it becomes apparent that Swan owners must themselves be prepared for the task of troubleshooting and isolating ailing radio circuitry.  In
order to carry out these future tasks, our motto "Know Thy Swan" is absolutely
the order of the day.

First off, the pioneers of Swan radio prepared operation and maintenance
manuals that included only a voltage chart for circuit values reference.
During that period which saw the single-bander, then the 240, 400, 350, 500
and 500C models, the engineering and technical writer staffs reasoned that
isolating defective components would be best accomplished through observation
of circuit voltages.  TIMES HAVE CHANGED!

Today, amateur radio enthusiasts do not routinely work with or experiment with
the lethal high voltages associated with vacuum tube radio equipment.
Therefore, for the sake of safety the most basic nonhazardous approach to
troubleshooting is resistance measuring.

This line of thinking requires that a resistance chart be produced showing the
measured values found while the radio was in good working condition.  Thus,
when something does go wrong beyond tube failure, there will be a means of
comparing working radio and non-working radio circuit resistance figures.

A resistance chart layout can look similar to the voltage chart shown in any
Swan manual.  In addition to listing all tubes for the given model to be
examined, include lines for K1 and K2 relays, VOX socket, Jones plug, and
accessory socket.  The resistance readings at these non-tube locations can be
important in many situations.  For example, each model of radio had 2 or more
series and the owner may not possess the schematic which relates to the series
on hand.  The model 350 (64-67) evolved through 4 series where the K1 relay in each series controlled different functions and/or switched different valued
components.  Also, K2 was a 2 pole relay in early and 3 pole in late 350
series transceivers.

Since there are 100 or more measurement points, it's not hard to make a
mistake somewhere in the process.  So, if one has the time (this is good
training, too!) make the measurements again and record them, comparing one to
the other.

Remember, all measurements are made with the power supply disconnected from the radio (and maybe stored in a separate room... You never Know!).  Do
whatever it takes through testing or calibration to make sure your ohm meter
is accurate as possible.

Next time we'll discuss voltage measurements..... K4BOV

Note:  Stu will be happy to help you with your technical questions.  You can
FAX him at (607) 936 2463, e-mail: radyojo@angelfire.com (or our collective e-mail: 
swanradio@xoommail.com) or to K4BOV with SASE.  Include serial numbers of equipment to be discussed.

******************************************************************************


SOMETHING FROM THE VAULT

                                   A Suggested Reprint From A Past Issue

I decided to reprint this article from one of our past issues because this
subject probably comes up more than any other.  If you have not seen it, I
think you will find it of value, and if you have, it will provide a good
refresher for you.

Reprinted from issue #3:

                           
                              SO, YOU WANT TO TUNE UP THE OLD RIG???

                                                     Dean/WA9AZK

Perhaps one of the most important things we can do to make our rigs last
longer and give the best performance is to keep them properly tuned and
aligned.  In general, the Swan manuals do a pretty good job of explaining the
alignment procedure.  There are, however, two areas I feel they could improve
upon, and after discussing these with "DR John," John Bruchey, he agrees.

Since Swan produced a myriad of transceivers, these "rules" will apply to the
more popular 350, 500 and 700 series (and perhaps others).  I have found them
to make alignment easier and more correct.  I have found the procedures
outlined in 270B and SW-240 manuals to be just fine.  If you have any other
experiences, please share them with the group.

Probably the area that misses the mark the most in the alignment procedure in
the manual(s) is the section dealing with peaking the VFO circuit.  The
book(s) suggest the placement of a volt meter (reverse polarity) between pin 1
of the 12BE6/receiver mixer, and ground.  The procedure then goes on to
explain that on a negative scale, peak the volt meter at certain frequencies,
etc.

If you have ever done this, you will notice that some of the circuits will not
clearly peak or that the maximum reading (minimum in this case) requires you
to totally remove one of the slugs from its form (I believe the 40M slug).  I
found this curious and talked to John about how he did it.  Here is what I
learned:

1.  Instead of connecting a volt meter as described, simply clamp a lead from
a field strength meter to the 30 pf capacitor which comes off of pin 1 of the
12BE6/Mixer (usually C0702) and adjust the slugs for maximum reading on the
same frequencies shown in the manual.  This will greatly simplify the
procedure and appears to be the most accurate way to align the circuit.  It is
not necessary to put the rig into the transmit mode for this adjustment.  You
should see a clear peak and I have found the circuit peaks when the slug is
well within the coil form.

2.  The other area I have found to be a better way to align at rig is in the
area of the Mixer and RF Driver circuits.  Instead of removing the screen
voltage by disconnecting a wire and measuring voltage across a 1K resistor,
etc.,  I use the following method:

A.  I do not disconnect the screen voltage.

B.  I do not use a volt meter.

C.  Instead, with the PA TUNE knob placed in the appropriate positions as
shown in the chart, and the rig tuned to the proper frequency and band as
shown in the same chart, I turn the mic gain down, use the PTT to activate the
transmitter circuit, inject a little carrier by offsetting the carrier
balance, and peak the driver as in normal tune-up.  Immediately resonate the
finals by dipping the current with the TUNE control.  I then peak each related
coil in the Mixer and RF Driver circuits, being careful not to exceed 100MA
cathode current and only transmitting for about 15 seconds.  If I do exceed
100MA, I simply adjust the carrier balance to minimize the current.

I have used this method to peak the Mixer and RF Driver circuits for years.
As a matter of fact, this method is suggested in other Swan manuals.  I
presume the reason Swan suggested you disconnect the screen voltage to the
finals and tune and tune these circuits as indicated was to help eliminate damage to the finals.

If you take a little care and avoid driving the finals too hard or too long, I
believe you will find this to be a superior and faster method.  Good luck and
any comments or additions will be appreciated....... Dean/WA9AZK

******************************************************************************

                                         TEN METERS CAN BE PESKY

One thing I forgot to mention in the original article above, was a suggestion
on how to solve problems that sometimes occur aligning your rig on 10 meters.

There have been times when a rig is so "twisted" out of alignment on the 10
meter circuits that it seems "I'll never bring the old gal back to proper
working order."  This has usually occurred when the well-intentioned owner
turns the slugs within the coil forms several revolutions.  Generally, most
circuits only need to be touched just a little.  Usually a 1/4 to 1/2 turn is
more than is needed.  This is especially true on 10 meters.

Since there are several places where the 10 meter slugs in both the Mixer and
RF Driver circuits will allow them to resonate like a Stratavarious violin,
the trick is to find the proper spot of resonance.  To do this, I use another
receiver and monitor the S-meter at the appropriate frequency of where the
dial on the transmitter is tuned, peaking each of the coils for maximum S-
meter reading.  

So, if you ever have a problem getting your Swan to perform on 10 meters as it
should (or for that matter any frequency), try this method.  It's save me a
lot of frustration many times..... Dean/WA9AZK

******************************************************************************

                                            POWER SUPPLY EXTRA

                                              Stu Morrison//K4BOV 

Introduced in 1965, the Swan 117X universal power supply remained in
production for more than a dozen years.  Without any change in design it was produced longer and in greater numbers than any other Swan product.

The "universal" meant it was capable of both AC and DC operation.  In order to
accomplish each mode using a single power supply, a rather interesting power
transformer was required.  

In this case, the 117VAC primary and high, medium and bias voltagesecondaries
are of familiar construction.  The low voltage winding; however, is actually
an 18VAC secondary with 9VAC and 12VAC taps.  With AC operation, the 12VAC tap is selected through connections at the 15 pin Jones connector and feeds filament, lamp and relay current to the appropriate output terminals.

For the DC mode, an inverter (the Model 14X or later 14C) is attached to the
rear of the power supply in place of the 15 pin Jones connector.  With 12VDC
applied, the inverter flip-flops (like an AC generator)  the battery voltage
across the entire 18VAC winding which is now operating as the PRIMARY.  All
output voltages exist just as with AC operation except the 117VAC winding has
become an unterminated secondary.  (If desired, light AC loads, such as a
lamp, solder iron, electric razor, etc., can be powered here when a proper
receptacle is mounted.)

The purpose of the foregoing was to point out the uniqueness of the 117X power transformer.  And, the probability of not locating an exact replacement should the original fail.  Well, with so few Swans going mobile these days, the
"universal" transformer is no longer an essential item.  Standard power supply
transformers can now be salvaged from other manufacturers equipment to
accommodate modern day needs.  In some cases it may be desirable to employ the complete power supply and/or speaker cabinet of another manufacturer.
                                                 
The power supplies listed below are capable of running most Swan transceivers
to at least the power levels indicated.  All need a 12 pin Jones plug
installed or existing plug rewired to conform with the Swan configuration.
Some require one or more minor changes to ensure correct output voltages.

Make/Model                                             SSB PEP Capability
------------------
---------------------------
Drake AC-3                                              325 Watts
Drake AC-4                                              325      "
EICO 751                                                 250      "
Galaxy PSA-300                                       700      "
Galaxy AC-35                                           400      "
Galaxy AC-48                                           250      "
Galaxy AC-384                                         600      "
Galaxy AC-400                                         700      "
Hallicrafters PS-150-120                            350      "
Hallicrafters PS-500                                   650      "
Heath HP-23                                              250      "
National AC-200                                       250      "
National NCXA                                         300      "
National AC-500                                       700      " (HV:
1100VDC)
Tempo AC ONE                                       375      "

.... Stu/K4BOV

******************************************************************************

                                                   MODEL TCU
                                  
                                            Transmitter Control Unit

                                                   (Full Picture)

General Description:

       Swan Electronics Corporation Model TCU Transmitter Control Unit is
designed to operate in conjunction with the Swan SW-240 Single Sideband Transceiver to provide:

                *  Separate VFO for non-transceive operation
                *  Extended coverage of the 80 meter CW band
                *  Reception of WWV or WWVH on 15 MC
                *  Voice Operated Transmission (VOX)
                *  100 KC Crystal Calibrator

      Minor modifications to the SW-240 are necessary.  All hardware,
modification parts, and mounting instructions are furnished with the TCU.  The complete unit is housed in a cabinet which matches the SW-240 Transceiver.  Provisions have been included to mount the SW-117B AC power supply within the TCU cabinet to provide a complete, compact installation with all of the desired operating features.

SPECIFICATIONS:

Frequency Coverage:            1.  WWV - 15MC
                                             2.  80M     3,500 to 3,650KC
                                             3.  75M     3,650 to 4,000KC
                                             4.  40M     7,000 to 7,300KC
                                             5.  20M   14.000 to 14,350KC

Front Panel Controls:              VOX Gain,  Anti-Trip,  Main Tuning,  VFO
                                              Selector,
                                             VFO Range,  Calibrate ON-OFF.

Audio Output:                         Audio output through built-in 3" by 5"
                                              speaker, or by phone jack on front panel.

Power Requirements:               All power requirements are supplied through
                                                a 12 conductor cable from the transceiver.

Dimensions:                           Width 13 1/4"  Depth 11"  Height 5 5/8"

Weight:                                  8 1/2 pounds without SW-117B power supply.

Note:  Rare complimentary 1963 Swan240 External VFO specification sheet.

                                              Stu/K4BOV

******************************************************************************

                                  Nets of Interest to Swan Collectors:

                                               (Current - 1999)


Swan User          Sunday          14.250      5PM eastern      WA9AZK   UT
Dean
                                                                              
W7RXG     UT   Norm
                                                                              
WA5BDR  NM   Jim

Swan Tech          Wednesday    14.251     2300GMT           K4BOV     NY
Stu

Swan Tech          Sat                   7.235     2-4PM eastern    K4BOV    NY
Stu & K1QQ      NJ    Kent
                                                                              
Other vintage equipment nets:

Collins Tech         Tuesday          3.955     8-9PM eastern    W3ST       PA
Dave

Hallicrafters          Saturday         7.280     1700GMT           WB8DML  OH
Jim

Hallicrafters          Sunday          14.293    1745GMT            VE4WI
CAN/Craig        

Vintage SSB        Sunday          14.293     2000GMT           WB0SNF  NE
Andy

Heathkit               Sunday          14.293     2030GMT           WB6LRG  CA
Don  


Swan Net Notes:  With the dramatic increase in Swan User Net session check-
ins, net control will now call for check-ins by time value needs, mobile
operation and by QTH area.

Swan Radio Network announcements and schedules:

<A HREF="http://www.geocities.com/latemod97">Swan Radio Network
</A> 
<A HREF="http://www.angelfire.com/ny2/hamradio/">Swan and Vintage Amateur
Radio TechLine</A> 
<A HREF="http://www.angelfire.com/ny2/hamradio/sell.html">Ham Radio
Sell/Trade/Want Listing</A>