## General User Requirements for Proposed Network

## District-Wide User Requirements

- Two LANs at each district and school site

- A WAN to supply connectivity between the LANs

- Should be fully functional for a minimum period of 7 to 10 years

- Internet access should be available for each site

- Should enable 100% growth in LAN throughput

- Should enable 2% growth in WAN throughput

- Should enable 10 times growth in District Internet throughput

- Data transport rates are 10BaseT 100BaseT and 100BaseFx

- Only two layer 3 and 4 protocols allowed namely, TCP/IP and IPX/SPX

#### LAN

- Star or extended star topology design

- Two segmented LANs at each site (schools and district)

- The segments will be designated as Administration and Curriculum

- 25 PCs per class room for curriculum purposes (24 student and 1 teacher)

- 75 PCs per site for administration duties

- Minimum data transport rates are 1.0 Mbps for hosts and 100.0 Mbps for servers

- 4 data cable runs 3 for curriculum

- Required horizontal cabling should be 100Mbps Cat5 UTP

- Required vertical cabling should be either Fibre Optic or Cat5 UTP

- Wiring should comply with EIA/TIA 568 standards

- POP (Point of Presence) to connect to WAN

- One MDF per site, only

- IDFs (as required) to be directly connected to MDF

- All router, switch, hub and server equipment, etc, are to be placed appropriately and physically secured

#### WAN

- Three regional hubs required forming the fast core WAN network

- The hubs comprise of the District Office, Service Centre and the Shaw Butte Elementary School

- Internet access will be via the District Office hub

- Internet connection through means of a frame relay link

- Routers at each core WAN location

- All outside access to the network will be denied through use of firewalls and ACLs.

#### Servers

- Should be sited according to function and anticipated traffic

- Each hub location should maintain a DNS server

- Each school should maintain a server for DNS and Email services

- DNS updates should flow form school to hub to District server

- District Master should be able to run queries to regional servers

- An administrative server at located at each school site should be available to teachers and staff

- An application server located at each school should provide software applications to any user

- A library server located at each school site should be available to any user

- Any other severs shall be sited according to user needs

#### Addressing Schematics

- District Office shall manage addressing convention scheme

- TCP/IP addressing convention scheme listings for all hosts and network devices

- IPX/SPX addressing scheme for network address listings

- Every device on administration network should employ static addresses

- Every curriculum networked PCs should utilise dynamic addresses assigned by the DHCP server