Power of Bulbs Experiment

AIM:	To discern the quantity of energy used by bulbs with different values of power

MATERIALS:

4 bulbs (21W, 24W, 36W & 48W), power-pack, energy counting device (flashes when 100 or 1000 joules used) will refer to as EC below, appropriate wires for connecting apparatus, chronometer (stopwatch)

DIAGRAM:

METHOD:

- Connect the apparatus as shown in the diagram, setting the EC

- Connect one of the bulbs, and close the circuit

- Record the number of flashes from the EC in one minute

- Replace the bulb with another and repeat steps 2 and 3

Repeat experiment until 3 sets of data is collected

SAFETY:

As this experiment involves electricity, care should be taken not to electrocute anyone, and no liquids should be allowed near the equipment.

RESULTS:

| 12V Bulbs | 1st set (J) | 2nd set (J) | 3rd set (J) | Average |
| --- | --- | --- | --- | --- |
| 21 Watts | 1600 | 1800 | 1800 | 1733 |
| 24 Watts | 1800 | 1800 | 1800 | 1800 |
| 36 Watts | 2500 | 2500 | 2500 | 2500 |
| 48 Watts | 3500 | 3600 | 3700 | 3600 |

CONCLUSION:

I conclude that the quantity of energy used by the bulb is directly proportional to the power of the bulb.

EVALUATION:

This was a simple experiment that had no problems. The device used to measure the energy used does have a special name, but I cannot remember it at the time of this writing.

# Text boxes

Energy Counter

To mains

Power-pack