Ohmic Non-ohmic Behaviour Experiment

AIM:		to discern the characteristic of three materials, and discern if they follow ohmic or non-ohmic behaviour of resistance (if ohmic, their characteristic on a graph is a straight line, as the value of resistance will be constant)

MATERIALS:

1 power-pack, wires for connecting, 1 ammeter, 1 voltmeter, 1 variable resistor, 1 Nichrome wire, 1 light bulb, 500ml of dilute H2SO4

DIAGRAM:

METHOD:

- Connect the apparatus as shown above

- Insert the nichrome wire

- Using the variable resistor, obtain a voltage of 1 V across the wire

- Record the value displayed by the ammeter

- Repeat steps 3&4 for the values of 2V-10V

- Repeat 3-5 until 3 sets of data are obtained

- Repeat steps 3-6 with the light bulb and the dilute H2SO4

SAFETY:

Care should be taken with the dilute H2SO4 as it is an acid. In the event of accidental contact with it, a mild alkaline powder should be applied. IT SHOULD NOT BE RINSED WITH WATER, as this will spread the acid. Care should be taken not to electrocute anyone and no water should be allowed near the equipment.

RESULTS:

| Conductor | V (Volts) | I (Amps) | Resistance |
| --- | --- | --- | --- |
|  |  | 1st | 2nd | 3rd | Average | (ohms) |
| Nichrome wire | 1 | 0.045 | 0.05 | 0.04 | 0.045 | 22.22 |
|  | 2 | 0.09 | 0.09 | 0.1 | 0.093 | 21.51 |
|  | 3 | 0.14 | 0.14 | 0.14 | 0.14 | 21.43 |
|  | 4 | 0.19 | 0.18 | 0.19 | 0.187 | 21.39 |
|  | 5 | 0.23 | 0.23 | 0.24 | 0.233 | 21.46 |
|  | 6 | 0.28 | 0.28 | 0.28 | 0.28 | 21.43 |
|  | 7 | 0.32 | 0.33 | 0.33 | 0.327 | 21.41 |
|  | 8 | 0.37 | 0.38 | 0.38 | 0.377 | 21.22 |
|  | 9 | 0.42 | 0.42 | 0.42 | 0.42 | 21.43 |
|  | 10 | 0.47 | 0.46 | 0.47 | 0.467 | 21.41 |
| Filament | 1 | 0.54 | 0.52 | 0.52 | 0.527 | 1.90 |
|  | 2 | 0.69 | 0.68 | 0.68 | 0.683 | 2.93 |
|  | 3 | 0.82 | 0.81 | 0.82 | 0.817 | 3.67 |
|  | 4 | 0.94 | 0.93 | 0.93 | 0.933 | 4.29 |
|  | 5 | 1.05 | 1.04 | 1.03 | 1.04 | 4.81 |
|  | 6 | 1.15 | 1.14 | 1.14 | 1.143 | 5.25 |
|  | 7 | 1.23 | 1.24 | 1.23 | 1.233 | 5.68 |
|  | 8 | 1.32 | 1.33 | 1.32 | 1.323 | 6.05 |
|  | 9 | 1.42 | 1.41 | 1.41 | 1.413 | 6.37 |
|  | 10 | 1.49 | 1.5 | 1.5 | 1.497 | 6.68 |
| Dilute H2SO4 | 1 | 0 | 0.01 | 0 | 0.003 | 333.33 |
|  | 2 | 0.02 | 0.02 | 0.03 | 0.023 | 86.96 |
|  | 3 | 0.04 | 0.05 | 0.04 | 0.043 | 69.77 |
|  | 4 | 0.06 | 0.04 | 0.06 | 0.053 | 75.47 |
|  | 5 | 0.05 | 0.06 | 0.05 | 0.053 | 94.34 |
|  | 6 | 0.05 | 0.06 | 0.06 | 0.057 | 105.26 |
|  | 7 | 0.06 | 0.06 | 0.06 | 0.06 | 116.67 |
|  | 8 | 0.07 | 0.08 | 0.07 | 0.073 | 109.59 |
|  | 9 | 0.11 | 0.1 | 0.11 | 0.107 | 84.11 |
|  | 10 | 0.13 | 0.14 | 0.13 | 0.133 | 75.19 |

CONCLUSION:

The conclusions drawn from the table is that the nichrome wire was the only object to follow ohmic behaviour. The filament of the light bulb and the acid did not follow ohmic behaviour. In the filaments case, the resistance increased with the temperature of the filament (increased by the current flowing through it) caused a change in the resistance. With the dilute H2SO4, however, the resistance was dependent on the number of ions to carry the charge across the acid. As the ions absorb some of the energy of the current in the process, this meant that the lower voltages lost energy while being conducted across, with the resistance being higher at those values

EVALUATION:

The results gathered for the dilute H2SO4 and the filament did not show the characteristics very well on the graph. More results should have been gathered, but the time taken to gather the present results was already extensive. I would recommend using different values of voltage to decrease the time, thus allowing a wider spectrum of results to be taken.

# Footnotes

Please note that this observation was made after the experiment was conducted during the analysis of the results. If it had been made earlier, I would have modified the experiment to reflect this.

# Text boxes

V

AS

Power-pack

Object